## Slide 1
Radar Detection Algorithms
Simulation, Clustering, Tracking & Classification

## Slide 2
Agenda
• Radar Detection Simulation
– Radar equation and received power modeling
– Point cloud generation algorithms
– Noise modeling and measurement simulation
• DBSCAN Clustering Algorithm
– Density-based spatial clustering
– Core points, border points, and noise
– Implementation and parameter tuning
• Multi-Object Tracking
– Nearest-neighbor data association
– Track lifecycle management
– Kalman filter prediction (linear motion)
• Classification Algorithms
– Rule-Based classifier with feature thresholds
– Naive Bayes probabilistic classification
– Model comparison and evaluation

## Slide 3
SECTION 1
Radar Detection Simulation

## Slide 4
Radar Equation - Received Power
Radar Equation
Pr(dBm) = K + 10·log₁₀(σ) - 40·log₁₀(R)
The radar equation calculates received signal power based on target RCS and range. K is a calibration constant (default: 81.2 dB).
1. Calculate range R from radar position to target (Euclidean distance in 3D)
2. Get target RCS (σ) based on object type and surface properties
3. Apply radar equation with path loss (-40·log₁₀(R) accounts for R⁴ loss)
4. Add Gaussian noise (shadow fading) with σ = 1.2 dB for realistic variation
5. Combine individual detection powers using linear summation (mW → dBm)

## Slide 5
Point Cloud Generation Algorithm
• Surface Sampling Strategy
– Sample points on visible surfaces (front/back, sides, top)
– Weight sampling towards radar-facing surfaces
– Apply corner reflector effect (2x RCS at corners)
• Distance-Based Scaling
– Closer objects → more detections (inverse relationship)
– At 10m: full detection count
– At 100m: ~25% of maximum count
• Per-Point RCS Distribution
– Total object RCS distributed across detection points
– Corner points receive higher RCS values
– Random variation factor (0.5x - 1.5x) for realism
• Noise Application
– Range noise: σ_r = 0.25m (Gaussian)
– Azimuth noise: σ_az = 0.2° (Gaussian)
– Radial velocity noise: σ_vr = 0.15 m/s (Gaussian)

## Slide 6
Detection Count by Object Type
Object Type | Length (m) | Width (m) | RCS σ (m²) | Min Detections | Max Detections
Car | 4.5 | 1.9 | 10.0 | 15 | 40
Truck | 10.0 | 2.6 | 30.0 | 30 | 80
Two-Wheeler | 2.2 | 0.8 | 3.0 | 5 | 12
Bicycle | 1.8 | 0.6 | 1.0 | 2 | 6
Pedestrian | 0.5 | 0.5 | 0.5 | 1 | 4

## Slide 7
SECTION 2
DBSCAN Clustering Algorithm

## Slide 8
DBSCAN - Density-Based Spatial Clustering
DBSCAN Algorithm
ε-neighborhood: N_ε(p) = {q ∈ D | dist(p,q) ≤ ε}
DBSCAN groups points based on density, separating clusters of arbitrary shape from noise without requiring the number of clusters a priori.
1. For each unvisited point p, retrieve its ε-neighborhood
2. If |N_ε(p)| ≥ minPts, p is a core point - start new cluster
3. Recursively expand cluster by adding all density-reachable points
4. If |N_ε(p)| < minPts and not reachable from core, mark as noise
5. Continue until all points are visited and labeled

## Slide 9
DBSCAN Point Classification
• Core Points
– Has at least minPts neighbors within ε distance
– Forms the dense interior of clusters
– Can expand the cluster by connecting to other core points
• Border Points
– Within ε of a core point but < minPts neighbors
– Belongs to cluster but cannot expand it
– Assigned to nearest core point's cluster
• Noise Points
– Not within ε of any core point
– Isolated detections (clutter, false alarms)
– Excluded from object tracking and classification
• Parameters
– ε (epsilon): 2.0m default - maximum neighbor distance
– minPts: 2 default - minimum samples for core point

## Slide 10
DBSCAN Implementation Details
• Distance Computation
– Euclidean distance: d(p,q) = √[(x₁-x₂)² + (y₁-y₂)²]
– Applied to world coordinates (x_w, y_w)
– O(n²) naive implementation, O(n log n) with spatial indexing
• Cluster Expansion (BFS)
– Use queue to track points to process
– When core point found, add all neighbors to queue
– Mark visited points to avoid reprocessing
– Continue until queue empty
• Feature Extraction per Cluster
– Centroid: mean(x), mean(y) of all points
– Extent: (max-min) in X and Y directions
– Statistics: mean/std of RCS and radial velocity
– Point count: number of detections in cluster

## Slide 11
SECTION 3
Multi-Object Tracking Algorithm

## Slide 12
Tracking Pipeline
Step 1
Prediction
Apply motion model to predict next state for all tracks
Step 2
Association
Match clusters to tracks using distance metric
Step 3
Update
Update matched tracks with cluster measurements
Step 4
Management
Create new tracks, delete old tracks

## Slide 13
Nearest-Neighbor Data Association
Greedy Association
cost(c,t) = ||centroid(c) - pos(t)||₂
Association matches new cluster measurements to existing tracks using distance-based cost minimization.
1. Compute cost matrix: distance from each cluster to each track
2. Sort all (cluster, track) pairs by cost (ascending)
3. For each pair in sorted order:
4. - If cluster and track are both unassigned AND cost ≤ threshold
5. - Assign cluster to track, mark both as used
6. Unassigned clusters → create new tracks
7. Unassigned tracks → increment miss counter

## Slide 14
Motion Model - Linear Prediction
• State Vector
– Position: (x, y) in world coordinates
– Velocity: (vx, vy) estimated from position changes
• Prediction Step
– x(t+dt) = x(t) + vx · dt
– y(t+dt) = y(t) + vy · dt
– Constant velocity assumption (no acceleration)
• Velocity Estimation
– vx = (x_new - x_old) / dt
– vy = (y_new - y_old) / dt
– Updated on each successful cluster association
• Track Lifecycle Parameters
– min_hits = 2: confirmations needed for valid track
– max_misses = 5: consecutive misses before deletion
– association_threshold = 5.0m: max distance for matching

## Slide 15
Track Lifecycle Management
• Track Creation
– New track created for each unassigned cluster
– Initial state: cluster centroid, zero velocity
– Status: tentative (hits = 1, age = 1)
• Track Confirmation
– Track confirmed when hits ≥ min_hits
– Only confirmed tracks used for classification
– Provides temporal consistency
• Track Update
– Position updated from associated cluster centroid
– Velocity estimated from position delta
– Feature history maintained (last 20 frames)
• Track Deletion
– Miss counter incremented on no association
– Track deleted when misses > max_misses
– Prevents ghost tracks from persisting

## Slide 16
SECTION 4
Classification Algorithms

## Slide 17
Classification Features
Feature | Description | Discriminative Power
num_points | Number of detections in cluster | High - varies by object size
extent_x | Width in X direction (m) | High - vehicle length indicator
extent_y | Width in Y direction (m) | Medium - vehicle width
mean_rcs | Average RCS in dBm | High - object reflectivity
std_rcs | RCS standard deviation | Low - surface uniformity
speed | Estimated velocity (m/s) | High - motion characteristics
mean_vr | Mean radial velocity | Medium - approach/departure

## Slide 18
Rule-Based Classification
Threshold Matching
score(c) = mean(match_scores) where match ∈ [0,1]
Classification based on predefined feature ranges for each class. Fast, interpretable, requires domain knowledge.
1. For each class, define (min, max) range for each feature
2. For input features, compute match score per feature:
3. - score = 1.0 if value in range (penalty for distance from center)
4. - score = max(0, 1 - distance/range_size) if outside
5. Average scores across features for class score
6. Select class with highest score
7. Confidence = best_score / sum(all_scores)

## Slide 19
Rule-Based Classification Thresholds
Class | Points | Extent X (m) | Extent Y (m) | RCS (dBm) | Speed (m/s)
Car | 10-50 | 1.5-6.0 | 1.0-3.0 | 10-35 | 0.5-40
Truck | 25-200 | 3.0-15.0 | 1.5-5.0 | 20-50 | 0.5-30
Two-Wheeler | 3-15 | 0.8-3.0 | 0.3-1.5 | 5-25 | 0.5-35
Bicycle | 1-8 | 0.5-2.5 | 0.2-1.2 | -5-20 | 0.3-15
Pedestrian | 1-6 | 0.2-1.5 | 0.2-1.0 | -10-15 | 0.1-3
Clutter | 1-5 | 0.0-1.0 | 0.0-1.0 | -20-20 | 0.0-0.5

## Slide 20
Naive Bayes Classification
Probabilistic Model
P(C|X) ∝ P(C) · ∏ P(xᵢ|C)
Probabilistic classifier assuming feature independence. Outputs confidence probabilities for each class.
1. Assume features are conditionally independent given class
2. Model each feature with Gaussian distribution: P(x|C) = N(μ_C, σ_C)
3. Compute log-likelihood for each class:
4. log P(C|X) = log P(C) + Σ log P(xᵢ|C)
5. Apply log-sum-exp trick for numerical stability
6. Normalize to get posterior probabilities
7. Select class with maximum posterior probability

## Slide 21
Naive Bayes Gaussian Parameters (μ, σ)
Class | Points | Extent X | RCS (dBm) | Speed (m/s) | Prior P(C)
Car | (25, 10) | (3.5, 1.0) | (22, 8) | (12, 6) | 0.35
Truck | (50, 20) | (8.0, 2.5) | (30, 8) | (10, 5) | 0.15
Two-Wheeler | (8, 4) | (2.0, 0.6) | (15, 7) | (10, 5) | 0.15
Bicycle | (4, 2) | (1.5, 0.5) | (8, 6) | (5, 3) | 0.10
Pedestrian | (2.5, 1.5) | (0.6, 0.3) | (5, 5) | (1.5, 0.8) | 0.10
Clutter | (2, 1) | (0.4, 0.3) | (10, 8) | (0.1, 0.1) | 0.15

## Slide 22
Rule-Based vs Naive Bayes Comparison
Rule-Based Classifier
• Fast computation (direct threshold checks)
• Highly interpretable (explicit rules)
• No training required
• Works well with domain expertise
• Binary matching (in range or not)
• Sensitive to threshold selection
• No probabilistic confidence
• Manual tuning for new scenarios
Naive Bayes Classifier
• Moderate computation (Gaussian PDF)
• Probabilistic output (soft decisions)
• Requires training data / parameters
• Data-driven parameter estimation
• Smooth probability gradients
• Handles feature overlap gracefully
• True confidence probabilities
• Adaptable through parameter updates

## Slide 23
Complete Classification Pipeline
Step 1
Detections
Raw radar detections with (x, y, vr, RCS)
Step 2
DBSCAN
Cluster detections into objects
Step 3
Tracking
Associate clusters, maintain track IDs
Step 4
Features
Extract cluster features for classification
Step 5
Classify
Apply Rule-Based or Naive Bayes model

## Slide 24
Feature History & Temporal Smoothing
• Feature History Storage
– Each track maintains last 20 frames of features
– Features stored per update: points, extent, RCS, speed, etc.
– Enables temporal analysis and trend detection
• Time-Averaged Features
– Classification uses averaged features for stability
– avg_feature = mean(feature_history)
– Reduces frame-to-frame variation
– More reliable classification for established tracks
• Classification History
– Track stores last 10 classifications
– Enables voting or consensus approaches
– Useful for detecting classification changes
• Benefits
– Reduces single-frame noise effects
– More consistent predictions over time
– Better handling of partial occlusions

## Slide 25
SECTION 5
Summary & Key Takeaways

## Slide 26
Algorithm Summary
• Radar Simulation
– Physics-based power calculation with radar equation
– Realistic point cloud generation on visible surfaces
– Configurable noise models for range, azimuth, velocity
• DBSCAN Clustering
– Density-based grouping without prior cluster count
– Separates objects from clutter/noise naturally
– ε = 2.0m, minPts = 2 for radar applications
• Object Tracking
– Greedy nearest-neighbor association
– Linear motion prediction for state estimation
– Track lifecycle with confirmation and deletion
• Classification
– Rule-Based: fast, interpretable, threshold-based
– Naive Bayes: probabilistic, adaptive, data-driven
– Feature-based: points, extent, RCS, speed

## Slide 27
Thank You
Questions?